## Slide 1
Step1: Take RS232 cable and 1 x mini jumper cap
Don’t plug in power cable. Open the unit , connect RS232 cable and put the cap to the two pins below

## Slide 2
Step 2: Run the Flymcu.exe software. Select port and AV1900 REV1.9 file

## Slide 3
Step 3: Push Start ISP(P) to update

## Slide 4
Step 4: When finished and shows “ok”, Unplug power cable and remove jumper cap. The firmware is updated.